design procedure for a common emmitter amplifier.

Setting the DC bias conditions.

What value do these resistors have to have?

first of all what value of DC collector current do I want
In order to keep dissipations low, I am going to set the collector current at about 10mA,
half of Vcc (7.5V) x 5mA = 38mW, this is okay in most resistors that I will use.

as the transistor will have a minimum hfe of about say 40, the 5mA collector current will give a base current of less than 0.12mA,

now I will design the potential divider on the input (or base) side of the transistor.
the purpose of this is to set the base voltage at about 1.5V,
this will set the emmitter at about 0.9V, as Vbe is about 0.6V.
We have already determined that the maximum base current will be about 0.12mA,
If I set the potential divider current at 1.2mA, then the base current will have little effect on the base voltage, the base voltage will be almost entirely set by the potential divider.
As the supply rail is 15V a divide by 10 will do here.
For convenience I will use values of 12k and 1.2k here..

This gives a divide by 11 rather than divide by 10, and hence sets the base at 15V /11 = 1.35V,
so the emmitter will sit at 1.35V - say 0.65V = 0.7V,

now to get an emmitter current of 5mA,
R= V/I = 0.7V/ 0.005A = 140 ohms,

now we want to drop about 7V in the collector resistor,
so R collector = V/I = 7V / 5mA = 1.4 k Ohms.

Setting the AC gain.....
With the emmitter resistor at 120 R, and the collector R at 1.4k we have a gain of 1400/120 =11.7
we can increase this by doing an AC bypass of some of this 140 R with a capacitor.
I will divide the 140R into 90R and 30R and bypass the 90R,
this gives a gain of 1.4k / 30R = 46.6
however as the below section shows for out calculation of gain we have to increase emmitter R to 35R so gain falls to 40.
the base current also reduces the gain.

Is the transistor internal emmitter resistance spoiling our calculations
In the above clculation we have to add the transistors internal emmitter resistance to the emmitter resistor component value.
The intrinsic emmitter resistance of the transistor is 25/ emmitter current in mA.
as I am setting emmitter current at 5mA, internal emmitter resistance will be 25 /5 = 5 Ohms.