# General comments
the output power tends to decrease with frequency, this may be due to the switch transition time, and deadtime, becoming a greater proportion of the cycle.
By adjusting the value of the resonant inductor the result for 400V supply and GaN FETs at 28Mhz has been maintained at over 90% efficiency.
the Siliconn carbide FET circuits give satisfactory results up to 14Mhz, but are struggling at 28Mhz.
The GaN FET circuits still give satisfactory results at 28Mhz.
However at 28Mhz the circuit performance is being affected by the parasitics of the FETs (output capacitance, switch delay times), so if using FETs from a different batch with different parasitics the inductor value would have to change

# Results using silicon FETs, 48V supply, and 1.84Mhz, 7Mhz and 14 Mhz.

The efficiency achieved is reducing as the frequency increases, this is because we have reduced but not removed the switching losses, and with higher frequency you switch more often.
simulation results for efficiency versus frequency, note that real circuit values will probably be lower than this.
1.84 Mhz 99.1%
7 Mhz 96.5%
14 Mhz 93.7%

The power throughput is also reducing as the frequency rises, this will be due to the proportion of the time that we spend switching rising as the freq increases.
so the proportion of the time that power is being transferred decreases as the frequency increases.
Simulation results for output power versus frequency.
1.84 Mhz 134W
7 Mhz 101W
14 Mhz 76W

# Results using Silicon Carbide FETs, 400V supply, and 1.84Mhz, 7Mhz, 14Mhz, and 28 Mhz

The efficiency achieved is reducing as the frequency increases, this is because we have reduced but not removed the switching losses, and with higher frequency you switch more often.
simulation results for efficiency versus frequency, note that real circuit values will probably be lower than this.
freq	efficiency with	efficiency with
adjusted L	L as resonant value
14 Mhz %	94%	90.5%
28 Mhz	92%	55%

The power throughput is also reducing as the frequency rises, this will be due to the proportion of the time that we spend switching rising as the freq increases.
so the proportion of the time that power is being transferred decreases as the frequency increases.
Simulation results for output power versus frequency.

14 Mhz	885W
28 Mhz	541W

# Results using GaN FETs, 400V supply, and 1.84Mhz, 7Mhz, 14Mhz, and 28 Mhz

The efficiency achieved is reducing as the frequency increases, this is because we have reduced but not removed the switching losses, and with higher frequency you switch more often.
simulation results for efficiency versus frequency, note that real circuit values will probably be lower than this.
freq	efficiency with	efficiency with
adjusted L	L as resonant value
1.84 Mhz	98.8%
14 Mhz	98.6%
28 Mhz	97.5%	78%

The power throughput is also reducing as the frequency rises, this will be due to the proportion of the time that we spend switching rising as the freq increases.
so the proportion of the time that power is being transferred decreases as the frequency increases.
Simulation results for output power versus frequency.
1.84 Mhz 1000W
14 Mhz 1012W
28 Mhz 702W