Description of the Boost SMPS topology

Firstly we look at the voltage applied to the inductor when the FET is on or off.
when the FET is on the input voltage is applied to the inductor.
when the FEt is off Vout-Vin is applied to the inductor, but in the opposite direction, this assumes that the inductor current is continuous.
What happens if the FET is not tunrned on at all, you will be able to see that the ouput is charged through the inductor and the diode,
and so ends up equal to the input voltage.

Now what happens if we start turning the FET on for say 5% of the cycle,
firstly we can say that during that 5% the inductor current will increase,
so the current flowing into the output capacitor for the rest of the cycle will also have increased,
so it makes sense that the output voltage is going to rise.

But what will be the new steady state output voltage, when the circuit eventually settles down.
The answer is that the steady state is when the average voltage applied to the inductor over one cycle is zero.
the voltage applied to the inductor during the on time is Vin,
and the voltage applied to the inductor during the off time is (Vin -Vout),
mathematically this is Vin x on time = (Vout-Vin) x off time.
and off time = 1 - on time, so we can say
Vin x on time = (Vout-Vin) x (1-on time)
as we call on time D, we can say
Vin x D = (Vout-Vin) x (1-D)

but we want to rearrange it as follows in order to get the output voltage.
Vin x D = (Vout-Vin) x (1-D)
or (Vout-Vin) = Vin x (D/(1-D))
you could say that we have boosted the output voltage above the input voltage, (hence the name of the topology),

eg. what happens if for example if we turn the FET on for 10% of the cycle.
now on time D= 0.1, and off time (D-1) = 0.9
put these numbers into the above equation to get
(Vout-Vin) = Vin x (D/(1-D)) = Vin x (0.1/(0.9)) = 11.1%
so output voltage will be 11.1% above the input voltage,
however it won't increase by quite that much as we have to allow for diode drops and resistive losses.

this calculation of Vout/vin only works if the inductor is big enough to keep the inductor and diode conducting during the off time.
if the diode stops conducting before the FET is turned back on, then the voltage at "V_drain" is no longer tied to the output voltage.

more

We have given the FET an on time of 40%, or D=0.4
from the equation
(Vout-Vin) = Vin x (D/(1-D))
that we have derived on the right, we get
(Vout-Vin) = Vin x (0.4/(1-0.4)) = Vin x 0.4/0.6= Vin x 0.666
or the output is the input boosted by about 67% - diode and resistive losses

for the steady state case the inductor current has to be the same at the start of every cycle,
so it has to be the same at the start and end of the cycle,
so for the steady state case, the voltage applied to the inductor over a cycle must average to zero.
As we apply +Vin when the FET is turned on,
we must apply -Ve volts when the FET is off,
this means that for the steady state case, Vout must be greater than Vin,
you could say that the output voltage has been boosted above the input voltage.

While the boost SMPS topology is often used with an AC input voltage to implement PFC,
this tends to result in quite a complex cct., so I am not doing that here.
This circuit here is deliberately being kept simple in order to explain the boost topology,
so it just uses a DC input voltage.